George Langstaff	GE 330

Laser Distance Measurements

There are many types of laser distance sensors.  Many of the applications are industrial in nature.  Keyence is a leader in this field and for this report, the Keyence LK series laser distance sensor was chosen.  A brief look at this product’s operation and specifications will help one to better understand laser distance measuring sensors in the large.  Below is a diagram of the LK-031 sensor head.

Figure 1.  Keyence LK-031 sensor head

Below are some useful facts about the LK series and how the operate:

- LK series are used for general purpose and high accuracy

- They measure distances using triangulation.

- A laser diode shines a beam of light to the target.

- The light will diffuse off the surface and back to the sensor.

- The light is focused onto a CCD (Charge Coupled Device) detector. As the target moves away from the sensor, the focused spot will move toward one end of the CCD. As the target moves toward the sensor, the focused spot will move toward the other end of the CCD.

- The position of the laser spot on the CCD is directly proportional to the distance to the target.

- Detects solids or liquids (opaque or transparent)

Found below in Figure 2 and Figure 3 are visual models of the sensors.

Figure 2.  How sensor operates			Figure 3.  PSD vs. CCD

The most important part of using these sensors is the interface with the processor.  The pin connections for this model can be found below in Figure 4.

Figure 4.  Pin connection diagram and explanations

The analog output is used to obtain the distance measurement. Figure 5 shows how this is done.

Figure 5.  Analog output characteristics

In order to get the output signal certain inputs, as described in Figure 4, must be supplied.  Timing diagrams can be found below in Figure 6.

Figure 6.  Input characteristics

Other important specifications for these sensors can be found in the table below.

Table 1.  Specifications for LK series

Some important features are:

- Use shielded output cable

- Resolution of 1 mm

- Minimum spot diamteter of 30 mm (accurate surface contour)

- Sampling time for the LK units

  - LK-031 = 512 ms

- Response speeds

  - Low speed = Averaging of 8 (8x512ms)

  - High speed = Average of 1 (1x512ms)

The LK series enables non-contact shape/thickness measurements of soft, thin or hot targets which cannot be measured with contact-type sensors at measurement ranges of 30 mm to 500.

For more information on these types of sensors:

- www.keyence.com

- www.acuityresearch.com

- www.micro-epsilon.com